## Slide 1: Modular Multi-ported SRAM-based Memories
Ameer M.S. Abdelhadi
Guy G.F. Lemieux

## Slide 2: Multi-ported Memories: A Keystone for Parallel Computation!
Enhance ILP for processors and accelerators, e.g.
  VLIW Processors
  CMPs
  Vector Processors
  CGRAs
DSPs
Major FPGA vendors provide dual-ported RAM only!
ASIC RAM compilers provide limited ports!

## Slide 3: Multi-ported SRAM Cell
ASICs / custom design only!
Increasing ports incurs higher delays and area consumption

## Slide 4: RAM Multi-pumping
Performance degradation
Data dependencies
Resources sharing
Low area

## Slide 5: Multi-banking
Divide memory into smaller banks
Distribute data using fixed hashing scheme
Access to same bank is resolved by multiple request
The Pentium (P5) has 8-way two port interleaved cache*
Area efficient
Long arbitration delays
Variable access latency
*[Alpert & Avnon, IEEE Micro, June 1993]

## Slide 6: Multi-read by Bank Replication
Example: Alpha 21264*
  Each integer cluster has a replicated 80-entry register file
  The 72-entry floating-point cluster register file is duplicated
  number of read ports is doubled
  Support two concurrent units each
*[Ditlow et al., IEEE ISSCC , Feb. 2011]

## Slide 7: Register-based Multi-ported RAM
Infeasible on Altera’s high-end Stratix V with our smallest test-case!
High resources consumption for deep memories (scaling)
High performance for small caches (<1k lines)

## Slide 8: LVT-based Approach
Stores the ID of latest written bank
LVT is a multi-ported RAM for banks IDs
  Implemented with registers
  Still has scaling issues: infeasible for deep memories!

## Slide 9: LVT-based Multi-ported RAM Example (1)

## Slide 10: LVT-based Multi-ported RAM Example (2)

## Slide 11: LVT-based Multi-ported RAM Example (3)

## Slide 12: XOR-based Multi-ported RAM*
SRAM-based
XOR is used to embed and extract data back: Embed: DATA=OLD⊕NEW Extract: DATA⊕OLD=OLD⊕NEW⊕OLD=NEW
*[Laforest et al. ACM/SIGDA FPGA, Feb. 2012]

## Slide 13: XOR-based Multi-ported RAM Example (1)

## Slide 14: XOR-based Multi-ported RAM Example (2)

## Slide 15: XOR-based Multi-ported RAM Example (3)

## Slide 16: XOR-based Multi-ported RAM Example (4)

## Slide 17: Motivation
 | #Registers | #BRAMs
Register-based LVT |  | 
XOR-based |  | 
Proposed I-LVT |  | 

## Slide 18: Motivation
 | #Registers | #BRAMs
Register-based LVT |  | 
XOR-based |  | 
Proposed I-LVT |  | 

## Slide 19: Motivation
 | #Registers | #BRAMs
Register-based LVT |  | 
XOR-based |  | 
Proposed I-LVT |  | 

## Slide 20: Method
Based on LVT approach
The LVT is a multi-ported RAM with constant inputs (bank IDs)
SRAM-based LVT
  Can be implemented with XOR-based multi-ported RAM
  Is generalized by the proposed I-LVT approach
  Two special cases are provided:
    Binary-coded I-LVT
    One-hot-coded I-LVT

## Slide 21: Method
Based on LVT approach
The LVT is a multi-ported RAM with constant inputs (bank IDs)
SRAM-based LVT
  Can be implemented with XOR-based multi-ported RAM
  Is generalized by the proposed I-LVT approach
  Two special cases are provided:
    Binary-coded I-LVT
    One-hot-coded I-LVT

## Slide 22: Method
Based on LVT approach
The LVT is a multi-ported RAM with constant inputs (bank IDs)
SRAM-based LVT
  Can be implemented with XOR-based multi-ported RAM
  Is generalized by the proposed I-LVT approach
  Two special cases are provided:
    Binary-coded I-LVT
    One-hot-coded I-LVT

## Slide 23: Method
Based on LVT approach
The LVT is a multi-ported RAM with constant inputs (bank IDs)
SRAM-based LVT
  Can be implemented with XOR-based multi-ported RAM
  Is generalized by the proposed I-LVT approach
  Two special cases are provided:
    Binary-coded I-LVT
    One-hot-coded I-LVT

## Slide 24: Method
Based on LVT approach
The LVT is a multi-ported RAM with constant inputs (bank IDs)
SRAM-based LVT
  Can be implemented with XOR-based multi-ported RAM
  Is generalized by the proposed I-LVT approach
  Two special cases are provided:
    Binary-coded I-LVT
    One-hot-coded I-LVT

## Slide 25: Invalidation Table Approach (I-LVT)
A bank for each write
A single write to a specific bank invalidates all the other banks
Feedbacks are received from all other banks
ffb generates a new data that contradicts all the other banks
fout detects the non-contradicting bank ID

## Slide 26: Invalidation Table Approach (I-LVT)
A bank for each write
A single write to a specific bank invalidates all the other banks
Feedbacks are received from all other banks
ffb generates a new data that contradicts all the other banks
fout detects the non-contradicting bank ID

## Slide 27: Invalidation Table Approach (I-LVT)
A bank for each write
A single write to a specific bank invalidates all the other banks
Feedbacks are received from all other banks
ffb generates a new data that contradicts all the other banks
fout detects the uncontradicted bank ID

## Slide 28: Invalidation Table Approach (I-LVT)
A bank for each write
A single write to a specific bank invalidates all the other banks
Feedbacks are received from all other banks
ffb generates a new data that contradicts all the other banks
fout detects the uncontradicted bank ID

## Slide 29: Invalidation Table Approach (I-LVT)
A bank for each write
A single write to a specific bank invalidates all the other banks
Feedbacks are received from all other banks
ffb generates a new data that contradicts all the other banks
fout detects the uncontradicted bank ID

## Slide 30: Bank ID Embedding: Binary-coded Bank Selectors
Feedback function for bank k:
Output function (all banks):

## Slide 31: Mutual-exclusive Conditions: One-hot-coded Bank Selectors
Feedback function for bank k:
Output function (check if condition match):

## Slide 32: Mutual-exclusive Conditions Examples
Each lines pair has a negated conditions
One and only one line is logically true

## Slide 33: One-hot/Binary Coded 2W/2R Example (1)
Condition:
Condition:

## Slide 34: One-hot/Binary Coded 2W/2R Example (2)
Condition:
Condition:

## Slide 35: One-hot/Binary Coded 2W/2R Example (3)
Condition:
Condition:

## Slide 36: One-hot/Binary Coded 2W/2R Example (4)
Condition:
Condition:

## Slide 37: 3W/2R I-LVT Implementation
Binary-coded I-LVT
One-hot-coded I-LVT

## Slide 38: SRAM Consumption
XOR-based consumes fewer SRAM cells if: (Unlikely!!)
Otherwise, one-hot consumes fewer SRAM cells than binary-coded if:
Register-based LVT | 
XOR-based | 
Binary-coded I-LVT | 
One-hot-coded I-LVT | 
Register-based LVT | 
XOR-based | 
Binary-coded I-LVT | 
One-hot-coded I-LVT | 

## Slide 39: Usage Guideline

## Slide 40: Experimental Environment
Different ~1k designs have been synthesized with various parameters sweep
  Altera’s Quartus II with Altera’s Stratix V device
Verified with Altera’s ModelSim
  Over Million RAM cycles for each configuration
Bypassing capability:
  New data read-after-write (same as Altera’s M20K)
  New data read-during-write (same as a single register)
Parameterized Verilog and simulation/synthesis run-in-batch manager are available online:
https://code.google.com/p/multiported-ram/

## Slide 41: Experimental Results BRAM Consumption
Compared to XOR-based approach:
  Average of 19%; up to 44% BRAM reduction
#BRAM compared to 32bit wide register-based LVT:
  Up to 200 % in XOR-based
  Up to 12.5% in I-LVT-based

## Slide 42: Experimental Results Fmax
Compared to XOR-based approach:
  Average of 38%; up to 76% Fmax increase
One-hot-coded I-LVT exhibits the highest Fmax
  Due to fast feedback paths
  BRAM consumption still within 6% of the minimal

## Slide 43: Conclusions
Modular multi-ported SRAM-based memories for embedded systems
Based on dual-ported BRAMs
Dramatically lower resources consumption and higher performance than previous approaches
  Close to register-based LVT BRAM consumption; No further significant improvement can be done
Additional features e.g. bypassing and initializing
Ready to use open source parameterized Verilog and a run-in-batch manager are available online
https://code.google.com/p/multiported-ram/