## Slide 1: Modular SRAM-based Binary Content-Addressable Memories
Ameer M.S. Abdelhadi and Guy G.F. Lemieux
Department of Electrical and Computer Engineering
University of British Columbia
Vancouver, Canada
a place of mind
THE UNIVERSITY OF BRITISH COLUMBIA

## Slide 2: Binary Content-Addressable Memory (BCAM)
Hardware-based Single-Cycle Parallel Search Engines
Write
Stores new data at specific address
Match
Search all addresses for a given data (pattern)
Found in ‘2’
B
C
D
A
0
1
2
3
BCAM
Search for ‘D’
B
C
D
A
0
1
2
3
BCAM
Store ‘C’ in ‘1’

## Slide 3: BCAM Applications
Memory management
Associative caches
Translation lookaside buffers (TLBs)
Databases
Networking
IP lookup in routing/ forwarding tables
Intrusion detection
Pattern matching
Data compression
Data encryption
find and shorten redundant patterns
find and encrypt specific patterns
e.g. DNA sequence lookup
Packet Classification
detect predefined suspicious packages
Eliminates memory bottleneck

## Slide 4: Motivation - FPGAs
1000’s
Memory
Blocks
100,000’s
Logic
Elements
No dedicated BCAM resources in FPGAs

## Slide 5: Objectives
FPGAs
Block RAMs are main storage
Limited memory bandwidth
BCAMs
Massively parallel memory search
Require high memory bandwidth
Use BRAMs to construct BCAMs
Modular and flexible
Storage efficient
Single-cycle
Performance oriented

## Slide 6: Algorithmic Heuristics
Associative Arrays
Hashes
Search Trees:
Tries, BSTs, …
Multi-unpredictable-cycle
Data dependent performance
Variable search depth
Misses due to conflicts

## Slide 7: Register-Based BCAM
Concurrent register read and compare
Single-cycle
Limited resources
Complex routing
Fits small BCAMs

## Slide 8: Brute-Force Transposed-Indicators-RAM (1) A Traditional BRAM-based BCAM
Key idea: Transposed RAM - data becomes addresses
Write
Write ‘0’ to location ‘B’
Match
Read location ‘D’ for match
‘2’
3
0
1
2
A
B
C
D
‘D’
3
0
1
2
A
B
C
D
‘0’ to ‘B’
* Xilinx App Notes

## Slide 9: Brute-Force Transposed-Indicators-RAM (2) Storing Data to Multiple Addresses
How can we store data to multiple addresses?
  Specify addresses using one-hot coding
  Each bit indicates a match or “store at location”
PROBLEM: Depth of CAM is limited by data width of RAM
  e.g. to build 1M deep CAM, we need 1M bits wide
  In FPGAs: 1000 BRAMs x 32bit wide = 32K deep CAM
BRAM-based
Single-cycle
Depth of CAM is limited by RAM width
1
3
2
1
0
D
C
B
A

## Slide 10: BCAM Cascading
PROBLEM:
  Patterns are encoded as RAM addresses
  RAM depth is exponential to pattern width
Solution: Cascading
  Divide pattern into smaller slices
  Search for each slice separately
  If all slices are found  pattern match!
  RAM depth is linear to pattern width
RAM Depth = 2Pattern Width
RAM Depth = 2Slice Width x (Pattern Width / Slice Width)
CAM
CAM
CAM
Slice
Slice
Slice
Matched Pattern
Slice Match
…
…
…
Slice Match
Slice Match
Pattern Match

## Slide 11: Hierarchical Search 2D BCAM (1) Narrow and Deep BCAM
Key idea: Hierarchical search
1D BCAM
2D BCAM
4M
too
deep
2k
2k
   Find a set (row) with match using a 1D BCAM
   Search this set (row) in parallel for a specific match

## Slide 12: Hierarchical Search 2D BCAM (2) Example
Divide address space into segments
  RAM: each segment in a line
  Transposed-RAM: indicates “pattern in segment?”
Hierarchical Search:
  Find a row (segment) with match using a 1D BCAM
  Search this row (segment) in parallel for a specific match
0
0
0
0
0
0
1
1
1
0
0
0
0
1
0
0
0
1
2
3
0
1
2
3
addresses
patterns
2
3
1
1
0
1
2
3
addresses
patterns
Transposed-RAM
RAM

## Slide 13: Hierarchical Search 2D BCAM (2) Example
Divide address space into sets
  RAM: each segment in a line
  Transposed-RAM: indicates “pattern in segment?”
Hierarchical Search:
  Find a row (segment) with match using a 1D BCAM
  Search this row (segment) in parallel for a specific match
0
0
0
0
0
0
1
1
1
0
0
0
0
1
0
0
0
1
2
3
0
1
2
3
addresses
patterns
2
3
1
1
0
1
2
3
addresses
patterns
Transposed-RAM
RAM

## Slide 14: Hierarchical Search 2D BCAM (2) Example
Divide address space into sets
  RAM: each set in a line
  Transposed-RAM: indicates “pattern in segment?”
Hierarchical Search:
  Find a row (segment) with match using a 1D BCAM
  Search this row (segment) in parallel for a specific match
0
0
0
0
0
0
1
1
1
0
0
0
0
1
0
0
0
1
2
3
0
1
2
3
addresses
patterns
2
3
1
1
0
1
sets
patterns
Transposed-RAM
RAM

## Slide 15: Hierarchical Search 2D BCAM (2) Example
Divide address space into sets
  RAM: each set in a line
  Transposed-RAM: indicates “pattern in set?”
Hierarchical Search:
  Find a row (segment) with match using a 1D BCAM
  Search this row (segment) in parallel for a specific match
0
0
0
1
1
1
0
1
0
0
1
0
1
2
3
sets
patterns
2
3
1
1
0
1
patterns
Transposed-RAM
RAM
sets

## Slide 16: Hierarchical Search 2D BCAM (2) Example
Divide address space into sets
  RAM: each set in a line
  Transposed-RAM: indicates “pattern in set?”
Hierarchical Search:
  Find a set (row) with match using a 1D BCAM
  Search this row (segment) in parallel for a specific match
0
0
0
1
1
1
0
1
0
0
1
0
1
2
3
patterns
2
3
1
1
0
1
patterns
Transposed-RAM
RAM
sets
sets
Match pattern ‘3’

## Slide 17: Hierarchical Search 2D BCAM (2) Example
Divide address space into sets
  RAM: each set in a line
  Transposed-RAM: indicates “pattern in set?”
Hierarchical Search:
  Find a set (row) with match using a 1D BCAM
  Search this set (row) in parallel for a specific match
0
0
0
1
1
1
0
1
0
0
1
0
1
2
3
patterns
2
3
1
1
0
1
patterns
Transposed-RAM
RAM
sets
sets

## Slide 18: Hierarchical Search 2D BCAM (3) Pros and Cons
Single match only
Cannot be cascaded
RAM depth is exponential to pattern width
Inefficient for wide patterns
BRAM-Based
Single-cycle
Efficient for deep CAMs

## Slide 19: Indirectly-Indexed 2D (II2D) BCAM (1) Cascadable Wide and Deep BCAM
PROBLEM: is it possible to regenerate matches for all addresses?
patterns
addresses
1
1
1
1
1
1
1
1
Match
Indicators

## Slide 20: Indirectly-Indexed 2D (II2D) BCAM (1) Cascadable Wide and Deep BCAM
PROBLEM: is it possible to regenerate matches for all addresses?
Key observation
Transposed RAM is a sparse matrix
n columns (set of addresses) accommodates n matches (1’s) at most!
patterns
addresses
1
1
1
1
1
1
1
1
Match
Indicators

## Slide 21: Indirectly-Indexed 2D (II2D) BCAM (1) Cascadable Wide and Deep BCAM
Key idea: use indirect indices to point to intra-set matches
Cascadable
Scalable (linear growth)
Supports wider patterns
PROBLEM: is it possible to regenerate matches for all addresses?
Key observation
Transposed RAM is a sparse matrix
n columns (set of addresses) accommodates n matches (1’s) at most!
patterns
Sets
1
1
1
1
1
1
1
1
Indicators
Indices
Intra-set Match Indicators

## Slide 22: Indirectly-Indexed 2D (II2D) BCAM (1) Cascadable Wide and Deep BCAM
Key idea: use indirect indices to point to intra-set matches
Cascadable
Scalable (linear growth)
Supports wider patterns
PROBLEM: is it possible to regenerate matches for all addresses?
Key observation
Transposed RAM is a sparse matrix
n columns (set of addresses) accommodates n matches (1’s) at most!
patterns
Sets
1
1
1
1
1
1
1
1
Indicators
Indices
BRAM
LUTRAM
Intra-set Match Indicators

## Slide 23: Indirectly-Indexed 2D (II2D) BCAM (2) Example
0
1
1
0
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
0
0
0
0
0
0
0
1
0
0
1
0
0
1
2
3
0
1
2
3
addresses
patterns
Transposed-RAM
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses

## Slide 24: Indirectly-Indexed 2D (II2D) BCAM (2) Example
0
1
1
0
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
0
0
0
0
0
0
0
1
0
0
1
0
0
1
2
3
0
1
2
3
addresses
patterns
Transposed-RAM
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses

## Slide 25: Indirectly-Indexed 2D (II2D) BCAM (2) Example
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
0
0
0
0
0
0
1
0
0
0
0
1
0
1
2
3
0
1
2
3
addresses
patterns
Transposed-RAM
Indicators-RAMs
0
1
1
0
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses

## Slide 26: Indirectly-Indexed 2D (II2D) BCAM (2) Example
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
-
-
-
1
0
-
0
1
0
1
0
1
2
3
sets
patterns
Transposed-RAM
Indicators-RAMs
0
1
1
0
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses

## Slide 27: Indirectly-Indexed 2D (II2D) BCAM (2) Example
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
-
-
-
1
0
-
0
1
0
1
0
1
2
3
sets
patterns
Transposed-RAM
Indicators-RAMs
0
1
1
0
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses
Match pattern ‘3’

## Slide 28: Indirectly-Indexed 2D (II2D) BCAM (2) Example
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
-
-
-
1
0
-
0
1
0
1
0
1
2
3
sets
patterns
Transposed-RAM
Indicators-RAMs
0
1
1
0
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses
Match pattern ‘3’

## Slide 29: Indirectly-Indexed 2D (II2D) BCAM (2) Example
Divide address space into sets
Store sets with a match in Indicators-RAM
Transposed-RAM stores indices to all matches in set
Hierarchical Search:
  Find indices of all matching sets in Transposed-RAM
  Read Indicators-RAM using indices from Transposed-RAM
-
-
-
1
0
-
0
1
0
1
0
1
2
3
sets
patterns
Transposed-RAM
Indicators-RAMs
0
1
1
0
2
3
3
1
0
1
2
3
patterns
RAM (reference)
addresses
Match pattern ‘3’
Found in ‘1’ and ‘2’
0
1
1
0
0
1
2
3

## Slide 30: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 31: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 32: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 33: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 34: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 35: Indirectly-Indexed 2D (II2D) BCAM (3) Area and Performance
Except for very a narrow HS, II2D exhibits higher Fmax
register-based BCAM register consumption
II2D linear ALM consumption; similar to other methods
HS exponential BRAM consumption
II2D linear BRAM consumption
II2D supports wider patterns

## Slide 36: Open Source
Modular and parametric Verilog files
Run-in-batch simulation and synthesis manager
http://ece.ubc.ca/~lemieux/downloads/

## Slide 37: Conclusions
Brute-Force Transposed-RAM
BRAM-based 
Single-cycle 
Deep 
Wide 
Cascadable 
patterns
addresses
Scalable 
Match
Indicators

## Slide 38: Conclusions
Hierarchical Search 2D BCAM
BRAM-based 
Single-cycle 
Deep 
Wide 
Cascadable 
patterns
sets
Scalable 
Set Match
Indicators

## Slide 39: Conclusions
Indirectly-Indexed 2D (II2D) BCAM
BRAM-based 
Single-cycle 
Deep 
Wide 
Cascadable 
patterns
sets
Scalable 
Intra-set Match Indicators
Indicators
Indices
Multi-unpredictable-cycle

## Slide 40: Thank You!

## Slide 41: Backup Slides

## Slide 42: Conclusions
II2D
Hierarchical
Brute-Force
patterns
addresses
Match
Indicators
patterns
s e t s
Match
Indicators
patterns
s e t s
Indicators
Indices
Match Indicators
BRAM-based   
Single-cycle   
Deep   
Wide   