## Slide 1: A Multi-Ported Memory Compiler Utilizing True Dual-port BRAMs
Ameer Abdelhadi and Guy Lemieux
Department of Electrical and Computer Engineering
University of British Columbia
Vancouver, Canada
a place of mind
THE UNIVERSITY OF BRITISH COLUMBIA
May 3rd, 2016

## Slide 2: Motivation (1): FPGAs as parallel accelerators
Used as parallel accelerators
  Have dual-ported memories only
1000’s
Dual-Ported
Block RAMs
1,000,000’s
Logic
Elements
1000’s
Multipliers/
DSPs

## Slide 3: Motivation (2) Mixed port requirements
Multi-porting approaches provide simple (fixed) ports only
Waste of resources if these ports are not active simultaneously

## Slide 4: Live-Value Table (LVT)
Multi-read
Replication
LVT with
2 write and
1 read ports
2-port RAM1
2-port RAM2
Multi-write
LVT
W0
W1
R
2-port RAM1
2-port RAM2
W
R0
R1
Easy!
Hard!
1
0
1
1
Always writes 0’s
Always writes 1’s

## Slide 5: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - stores data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 6: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - stores data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 7: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - store data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 8: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - store data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 9: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - store data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 10: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - store data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool

## Slide 11: Data Banks Optimization
LVT-based multi-ported RAM is composed of:
  LVT - tracks changes
  Data banks - store data copies
Our previous work (I-LVT/ FPGA’14) optimizes LVT only
This work
  Optimizes the data banks (not the LVT!)
  The first technique that requires a CAD tool
  This work solves the final step and most important problem of Block RAM allocation

## Slide 12: Mixed Port Requirements (1): Fixed ports
Fixed (simple) ports:
The majority of multi-ported memories supports fixed ports only

## Slide 13: Mixed Port Requirements (2): True ports
True ports:
Some techniques support the construction of multi-true-ports
BRAMs in FPGAs are true dual-ported

## Slide 14: Mixed Port Requirements (3): Switched ports
Switched ports:
A number of writes are switched with a number of reads
True ports are special case of switched ports

## Slide 15: Switched Ports (1) Example
Key Observation:
BRAMs’ true ports can be utilized to optimize switched ports
Objectives:
Optimize the construction of multi-switched ports

## Slide 16: Switched Ports (2) Fixed ports abstraction

## Slide 17: Switched Ports (3) Fixed data banks

## Slide 18: Switched Ports (4) DFG modeling

## Slide 19: Switched Ports (5) Switched DFG

## Slide 20: Switched Ports (6) DFG Covering

## Slide 21: Switched Ports (6) DFG Covering

## Slide 22: Switched Ports (6) DFG Covering

## Slide 23: Switched Ports (6) DFG Covering

## Slide 24: Switched Ports (6) DFG Covering

## Slide 25: Switched Ports (6) DFG Covering

## Slide 26: Switched Ports (6) DFG Covering

## Slide 27: Switched Ports (6) DFG Covering

## Slide 28: Switched Ports (7) Switched data banks

## Slide 29: Switched Ports (7) Switched data banks

## Slide 30: Switched Ports (7) Switched data banks
12 BRAMs
8 BRAMs
(33% reduction)

## Slide 32: Multi-switched-ports Compiler
A RAM compiler optimizes data banks construction
  Generates DFG from port requirements
  Solves set-covering problem on all edges
    Covers are predefined biclique patterns
    Solved as BLP problem
  Generates Verilog modules based on optimal covering
  Available as open source contribution
  https://github.com/AmeerAbdelhadi http://www.ece.ubc.ca/~lemieux/downloads/
  Supports bypassing (RAW & RDW) and Initialization

## Slide 33: Graphical User Interface (GUI)

## Slide 34: Source of inspiration: Multi-True-Ports by Choi et al. / UofT
Provides true ports only (no simple/fixed ports)
Is a special case of our generalized approach
Doesn't need a CAD tools

## Slide 35: Experimental Results
Run-in-batch flow manager
  Uses Altera’s Quartus II for synthesis on Stratix V
  Uses Altera’s ModelSim for verification with:
    Random vectors
    Over a million RAM access cycles
Results on random test-cases
  Up to 8 switched ports
  Up to 4 writes and 4 reads per switched port
  Up to 28 writes/reads per test-case
 | Average BRAM Reduction | Average ALMs Reduction | Average Fmax Increase
Best of Previous | 18% | -3% | -1%
True Ports | 42% | 53% | 15%

## Slide 36: Conclusions
A methodology to support switched write/read functionality
True dual-ported BRAMs are utilized to optimize the RAM allocation
A RAM compiler optimizes the problem
An additional 18% average BRAM reduction compared to the best of other approaches
Practical solution:
  Initialization
  Bypassing
  Available as open source

## Slide 37: Future Directions
Applications
  Parallel computation
  HLS – storage binding
Optimization of switched ports port assignment
  Extraction of mutually-exclusive functions from HDL
Statistical approach
  Ports which are mutually-exclusive in most cases can use a switched port
  Access conflicts will be rare

## Slide 38: Thank You!