## Slide 1: Safe Overclocking of Tightly Coupled CGRAs and Processor Arrays using Razor
© 2012 Guy Lemieux
Alex Brant, Ameer Abdelhadi, Douglas Sim, Shao Lin Tang, Michael Yue, Guy Lemieux
The University of British Columbia

## Slide 2: Overclocking… is it safe?
Clock frequency determined by 2 things:
  CAD timing analysis (timing margins)
  speed binning of actual wafers + chips (variation)
Can you go faster?
  Yes, if your chips are fast
  Yes, if your data is not “worst-case”, eg carry propagation
  Yes, if you do not want “safe” timing margin guardbands

## Slide 3: Overclocking… is it safe? 3.8GHz 4.2 V
3.818GHz !!!
4.210V

## Slide 4: Overclocking… is it safe?
How fast is too fast?
  Blows up
  Fails to POST
  Fails to boot
  Blue screen of death
  Random crashes
  Data errors in documents and spreadsheet
When these problems go away, is it safe?

## Slide 5: Overclocking… is it safe?
Root cause: timing errors
  Problem 1: can we detect them?
    Yes, e.g. using Razor
  Problem 2: can we correct them?
    Yes, using Razor with feed-forward pipelines
      Pipeline must be ‘replayed’, input data ‘unfetched’
    Not possible with general sequential logic
      Need ‘spare’ cycles to ‘unfetch’ input data
      Cyclic dependencies make this difficult

## Slide 6: Overclocking… is it safe?
If not for general logic, what about…
  Traditional CPU pipelines? Yes:
    Feed-forward, correctable by Razor-replay
  Multi-core CPUs? Yes:
    Each CPU is a traditional pipeline
    Loosely coupled
      Other CPUs tolerate race conditions

## Slide 7: Overclocking… is it safe?
If not for general logic, what about…
  Ambric-style processor arrays? Yes:
    Like multi-core CPUs
    Loosely coupled
      Neighbour CPUs tolerate uncertainty of arrival time
  Tightly coupled processor arrays or CGRAs? No: neighbour CPUs cannot tolerate delays!

## Slide 8: Main Contribution
Extends Razor error correction to…
  tightly coupled processor arrays, CGRAs
  time-multiplexed FPGAs/CGRAs
  Tightly coupled means…
    Pre-scheduled communication
      Data must be present during cycle X
    No “data presence” indicators / handshakes

## Slide 9: Razor FF

## Slide 10: Razor FF in Pipeline
clk
clk + delay

## Slide 11: Razor FF in Pipeline

## Slide 12: How can we overclock?
10+9+8 = 27ps clock

## Slide 13: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 14: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 15: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 16: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 17: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 18: How can we overclock?
9+8 = 17ps clock, most of the time

## Slide 20: Array Architecture
Tightly coupled communication:
- can be FIFO-based or ‘mailbox’-based
Fully bypassed:
- write on cycle X
- read on cycle X+1, ie address provided cycle X

## Slide 21: Add “Razor” to Block RAM

## Slide 22: Processor Error Detection (for East direction only)
Processor memory error:
Causes stall
Incoming stall (from N,S,W):
produces
Outgoing E stall
Early warning signal:
prevents incoming data

## Slide 23: Processor Error Detection (all four directions)

## Slide 24: Writes entering error region….
t+1: AB || BC ;
t+2: BC ;

## Slide 25: Razor Stall Propagation (1D)

## Slide 26: Razor Stall Propagation (1D)
1
time
X

## Slide 27: Razor Stall Propagation (1D)
1
time
X

## Slide 28: Razor Stall Propagation (1D)
2
1
time
X
X

## Slide 29: Razor Stall Propagation (1D)
2
1
time
X
X

## Slide 30: Razor Stall Propagation (1D)
2
1
time
X
X

## Slide 31: Razor Stall Propagation (1D)
2
1
time
X
X

## Slide 32: Razor Stall Propagation (1D)
2
1
time
X
X

## Slide 33: Razor Stall Propagation (1D)
3
2
1
time
X
X
X

## Slide 34: Razor Stall Propagation (1D)
3
2
1
time
X
X
X

## Slide 35: Razor Stall Propagation (1D)
3
2
1
time
X
X
X

## Slide 36: Razor Stall Propagation (1D)
3
2
1
time
X
X
X

## Slide 37: Razor Stall Propagation (1D)
3
2
1
time
X
X
X

## Slide 38: Razor Stall Propagation (1D)
3
2
1
time
X
X
X
3 Errors Detected
2 Stalls to Correct
# STALLS < # ERRORS
Might be
scalable!!

## Slide 39: Razor Stall Propagation (2D)

## Slide 40: Razor Stall Propagation (2D)
X

## Slide 41: Razor Stall Propagation (2D)
X

## Slide 42: Razor Stall Propagation (2D)
X
X

## Slide 43: Razor Stall Propagation (2D)
X
X

## Slide 44: Razor Stall Propagation (2D)
X
X
X

## Slide 45: Razor Stall Propagation (2D)
X
X
X

## Slide 46: Razor Stall Propagation (2D)
X
X
X

## Slide 47: Razor Stall Propagation (2D)
X
X
X

## Slide 48: Razor Stall Propagation (2D)
X
X
X

## Slide 49: Razor Stall Propagation (2D)
X
X
X

## Slide 50: Razor Stall Propagation (2D)
X
X
X

## Slide 51: Razor Stall Propagation (2D)
X
X
X
3 Errors Detected
2 Stalls to Correct
# STALLS < # ERRORS
Might be
scalable!!

## Slide 52: Manual experiment: # stalls vs # errors
# errors
# stalls

## Slide 53
Monte Carlo Simulations…

## Slide 54: Stalls vs Errors (N x N array)

## Slide 55: Recovered Utilization (N x N)

## Slide 56
Experimental Results…

## Slide 57: Experimental Results
Build Processor Array on FPGA…
  2 x 2 array in silicon (running)
  3 x 3 array in simulation (verification)
Static critical path always through ALU + communication channels
  Typically multipilier, but only if used (!)
  Depends upon values being multiplied
Overclock system
  Fmax depends upon multiplier use, data values

## Slide 58: Place & Route Results
Area analysis for processor
  2,958 ALMs + 304 Regs (baseline)
  3,082 ALMs + 517 Regs (with Razor)
Static timing analysis for array
  90 MHz (baseline)
  88 MHz (with Razor)
Overhead is very low (4% ALMs)

## Slide 59: System under Test

## Slide 60: Methodology (baseline)
Run once: circuit at low speed
  Record correct output vectors
For increasingly higher clock speeds
  Run circuit with input test vectors
  Fail on first error
Remember highest clock speed

## Slide 61: Results (baseline)
Benchmark | Static Timing (CAD) | Overclocked (1st error)
Random | 90 MHz | 135 MHz
Mean | 90 MHz | 121 MHz
Wang | 90 MHz | 131 MHz
PR | 90 MHz | 136 MHz
average | 90 MHz | 130.4 MHz
Processor arrays can be overclocked
  Amount depends on application + data + chip
But is it safe?
  Our “test jig” tested results offline to find errors
  Unsafe! baseline cannot detect errors

## Slide 62: Methodology (Razor)
Run once: circuit at low speed
  Record correct output vectors
For increasingly higher clock speeds
  For increasingly higher shadow FF delay
    Run circuit
    Record # errors, # corrected errors, # stalls
Remember highest throughput

## Slide 63: Results (baseline)
Benchmark | Static Timing (CAD) | Overclocked (runs past 1st error) | Stall Rate
Random | 88 MHz | 163 MHz | 5.0%
Mean | 88 MHz | 144 MHz | 1.3%
Wang | 88 MHz | 147 MHz | 0.7%
PR | 88 MHz | 145 MHz | 1.7%
average | 88 MHz | 149.4 MHz | 2.0%
Processor arrays can be overclocked
  Even higher rates past 1st error
  Errors require stalls to correct, lowers thru-put
  Stop increasing Fmax after thru-put peaks

## Slide 64: Results (new Razor)
Benchmark | Static Timing (CAD) | Overclocked (runs past 1st error) | Stall Rate
Random | 88 MHz | 163 MHz | 5.0%
Mean | 88 MHz | 144 MHz | 1.3%
Wang | 88 MHz | 147 MHz | 0.7%
PR | 88 MHz | 145 MHz | 1.7%
average | 88 MHz | 149.4 MHz | 2.0%
But is it safe?
  Safe! Razor detects and corrects errors
  Our “test jig” tested results offline to verify the errors were corrected

## Slide 65: Results (Comparison)
Benchmark | Baseline STA (safe) | Razor-Corrected Effective Throughput | Speedup
Random | 90 MHz | 155 MHz | 1.72 x
Mean | 90 MHz | 142 MHz | 1.58 x
Wang | 90 MHz | 146 MHz | 1.62 x
PR | 90 MHz | 143 MHz | 1.59 x
average | 90 MHz | 146.5 MHz | 1.63 x
Processor arrays can be safely overclocked
  63% higher throughput
Low area cost (+4% ALMs)

## Slide 67: Observations / Notes
Time-multiplexed CGRAs/FPGAs can also benefit
  Just reserve 1-2 clock cycles in the time-mux schedule for error recovery
Loosely coupled processor arrays can be overclocked locally
  Just add Razor to each processor
  No need to propagate stall signals; automatically done through data presence indicators

## Slide 68: Summary / Conclusions
Processor arrays can be safely overclocked
  Even with very tightly scheduled communication
Processor arrays are scalable
  Errors produce stall wavefronts
  Several wavefronts merge into a single stall cycle
Throughput increased 63% on average
  Speedup depends upon benchmark, data values